## Slide 1
DNR COLLEGE
DEPARTMENT OF MICROBIOLOGY
Presented by:
R.SAKUNTALA
Lecturer In Microbiology

## Slide 2
sewage
Sewage is waste water from community, containing solid & liquid excreta, derived from houses, street & yard washings, factories & industries.
Sullage:
Waste water which does not contain human excreta.

## Slide 3
  Amount of sewage that flows in sewers depends upon:
  Habits of the people
  Time of the day
  The average amount of sewage which flows through the sewerage system in 24 hours is called the "dry weather flow"

## Slide 4
Health aspects
Environmental problems:
Creation of nuisance, unsightliness & unpleasant odours
Breeding of flies & mosquitoes
Pollution of soil & water supplies
Contamination of food
Increase in the incidence of disease

## Slide 5
Composition of sewage
99.9% water
0.1% - Solids (Organic & inorganic) (suspension & solution)
Offensive odour is because of decomposition of organic matter
1 gm of faeces contains 1000 million of E. coli, 10 to 100 million of faecal streptococci & 1 to 10 million spores of Cl. Perfringens.

## Slide 6
strength" of sewage
Biochemical Oxygen Demand (BOD): Amount of oxygen absorbed by a sample of sewage during a specified period, generally 5 days, at a specified temperature, generally 20° C for the aerobic destruction or use of organic matter by living organisms.
If the BOD is 300 mg/L & above - strong 100 mg/L – weak
Chemical Oxygen Demand (COD): measures the oxygen equivalent of that portion of the organic matter in a sample which is susceptible to oxidation by a strong chemical oxidiser. Suspended Solids: 100 mg/L - weak ►500 mg/L - strong

## Slide 7
Decomposition of organic matter
1. Aerobic process:
Most efficient method of reduction of sewage
Requires continuous supply of free dissolved oxygen
Organic matter is broken down into simpler compounds like CO₂, water, ammonia, nitrites, nitrates & sulphates by the action of bacterial organisms including fungi & protozoa

## Slide 8
Anaerobic process:
Effective when sewage is highly concentrated & contains plenty of solids.
End products of the decomposition are methane, ammonia, CO₂ & H2.
Reactions are slower & mechanism of decomposition extremely complex

## Slide 9
Screening
Metal screen - to intercept large floating objects like pieces of wood, rags, masses of garbage & dead animals - to prevent clogging.
Screen consists of vertical or inclined steel bars set at 5 cm apart.
Screenings are removed from time to time, either manually or mechanically & disposed off by trenching or burial.

## Slide 10
Sludge digestion
If incubated under favourable conditions of temperature & pH, it undergoes anaerobic auto-digestion in which complex solids are broken down into water, CO₂, methane & ammonia. Volume is reduced. Takes 3-4 weeks or longer Residue is inoffensive, sticky & tarry mud which will dry readily & form excellent manure. Methane gas released can be used for heating & lighting purpose