## Slide 1: Ion selective electrode (ISE)
B.Madhavi
Asst.Professor
Dept.of P.G.Chemistry
D.N.R.College
Bhimavaram

## Slide 2: Introduction
Ion selective electrode (ISE) is an analytical technique used to determine the activity of ions in aqueous solution by measuring the electrical potential.
Specific ion dissolved in a solution create an electrical potential, which can be measured by a voltmeter or pH meter.
The strength of this charge is directly proportional to the concentration of the selected ion.

## Slide 4: Principle
ISE consists of a thin membrane
Only specific ion can be diffuse.
By measuring the electric potential generated across a membrane by “selected” ions, and comparing it with reference electrode.
And net charge is determined.

## Slide 5: Potentiometry
Potentiometry
  Use of Electrodes to Measure Provide Chemical concentration
Voltages
that
Indicator Electrode:
Electrode that responds to analyte
Reference Electrode:
Second ½ cell at a constant potential
Cell voltage is difference between the indicator and reference electrode

## Slide 6: Reference Electrode
Silver-Silver Chloride Reference Electrode

## Slide 7: Types of ISE
Glass membrane
Solid state electrode
Liquid based electrode
Compound electrode

## Slide 8: Glass Membrane Electrode
This method uses the electrical potential of pH-sensitive electrodes as a measurement signal.
The glass electrode is the most commonly used sensor.
Not having the disadvantages of the optical methods, it can be used almost universally.

## Slide 9: Solid State Electrode
Electrode body of Inorganic crystalline polymer.
E.g. Special Epoxide Resin with excellent mechanical properties.
High temperature stability.

## Slide 10: Liquid based electrode
Formed by a very thin layer of an organic liquid.
Membrane is like jelly
Impermeable to water
only to allow to pass certain ion.
Organic material
  Carbon tetrachloride
  Benzene
  Mesitylene

## Slide 11: Compound electrode
Electrode have membrane of multiple type

## Slide 12: Electrolytes
Type of ions
  Cations – Positive charge
    move toward the cathode
Na+ = Extracellular – Brain Activity
K+ = Intracellular – Heart & Muscle
Ca+ = Extracellular – Heart & Muscle
H+ = Extracellular - Acidic
Anions – Negative charge
  move toward the anode
Cl – Extracellular
HCO–3 – Extracellular - Basic
12

## Slide 13: Sample Collection
Serum
  Collected in heparin bulb
  Plain
  EDTA can not be use for doing electrolyte
    EDTA is chelating agent & anti-coagulant.
    It chelat with all ions of blood
    So interfere with concentration of ions
Urine
  Collected in plain vacuette
13

## Slide 14
Types of Heparin vacuette
Ammonium
Lithium = Lithium+ heparin
Sodium=Sodium+ heparin For measure the sodium
lithium heparin vacuette
ammonium heparin vacuette
Use of sodium vacuette gives false high sodium concentration.

## Slide 15: Routinely measured electrolytes
Sodium
(90%)Major cation
Extracellular fluid outside cells Normal values
Serum = 135-145 mEq/L
Urine (24 hr ) = 40-220 mEq/L
Functions
Influence on regulation of body water
Osmotic activity
Central - Neuromuscular activity
15

## Slide 16: Hyponatremia
16
Hyponatremia <135 mEq/L
  Increased Na+ loss
  Causes
    Diabetes mellitus
    Diabetic Ketoacidosis
–- Because of diuresis
    Severe diarrhea & Severe Vomiting

## Slide 17: Hypernatremia
Excess water loss
resulting in
dehydration (relative increase)
Dehydration from inadequate intake
Dehydration due severe diarrhea
Diabetes insipidus
Burns
water
17

## Slide 18: Potassium (K)
(2%)major cation
Intracellular fluid inside cell Normal value
Serum- 3.5-5.3 mEq/L
Urine- 25-125 mEq/L
Function
Heart muscle contraction
Increase or Decrease K+ = Arrhythmiasis
18

## Slide 19: Hypokalemia
Hypokalemia = a low level of potassium (K+) in the blood serum.
Diarrhea
Medications like furosemide (diuretic)
Dialysis
Diabetes insipidus
Hyperaldosteronism

## Slide 20: Hyperkalemia
Increased K concentration
Causes
  Acute Renal failure
  Chronic Renal failure
  Acidosis (Diabetes mellitus )
    H+ competes with K+ to get into cells & to be excreted by kidneys
    Decreased insulin promotes cellular K loss
    Hyperosomolar plasma (from ↑ glucose) pulls H2O and potassium into the plasma .
20

## Slide 22: Chloride ( Cl - )
Chloride
Major cation Extracellular fluid
Normal value
Serum – 100 -110 mEq/L
24 hour urine – 110-250 mEq/L varies with intake
CSF – 120-132 mEq/L
22

## Slide 23: Hypochloremia
Same as Hyponatremia
congestive heart failure
Severe diarrhea
Severe vomiting
drugs such as
  Laxatives
  diuretics
  corticosteroids
  Bicarbonates.
23

## Slide 24: Hyperchloremia
Same as Hypernatremia
Increased serum Cl
  dehydration
  renal tubular disease
  metabolic acidosis
24

## Slide 25: Advantages
Good Linearity
Good precision
Less chance of damage
No consumption require
Non-contaminating.
Fast analysis.
Less interference from turbidity.
serum color &

## Slide 26: Limitations
Electrodes can be block by proteins.
Interference by other ions.
Electrodes are fragile
Limited electrode life – 3 to 4 months.

## Slide 27: Application of ISE
Electrolyte
  Sodium
  Potassium
  Calcium
  Lithium
  Iodine
  Magnesium
  Chloride
  Fluoride
Glucose
Urea
Arterial Blood Gas Analysis
  pO2
  pCO2
  pH
  HCO3-
27

## Slide 28: THANK YOU